## Slide 1
Version 2.10 OCT 2014
Basic Radio Communications
LO2 Part 2
Be able to send messages on the Air Cadet radio network
Uncontrolled copy not subject to amendment

## Slide 2: Radio Checks
Signal Strength:
LOUD The strongest signal
GOOD
WEAK
VERY WEAK The weakest signal
FADING Loud to very weak
Notes: Message Sending
RADIO CHECK
1. When a radio station first switches on it is necessary to establish if communications are satisfactory. The operator should carry out a "Radio check" to achieve this. A radio check is a two-way communication which reports on two aspects of the transmission, its strength and readability. The strength of a signal is divided into 5 levels or degrees. They are:
Loud (The strongest signal)
Good
Weak
Very weak (The weakest signal)
Fading (Signal strength fades and parts of the transmission can not be heard)

## Slide 3
Readability:
CLEAR Excellent Signal
READABLE Satisfactory
UNREADABLE Not readable
DISTORTED Difficult to hear
INTERMITTENT Goes on and off
INTERFERENCE Background noise
Radio Checks
Notes: RADIO CHECK
2. Readability is the capacity of understanding and has six different grades or degrees which are:
Clear (Excellent Signal)
Readable (Satisfactory)
Unreadable (You an not be understood)
Distorted (Difficult to hear)
Intermittent (Signal goes on and off)
Interference (Difficult to hear because of background noise)

## Slide 4
    MRG91 - this is MRG84 radio check - over
    MRG84 - this is MRG91 good readable radio check - over
    MRG91 - this is MRG84 loud clear - out
Radio checks can be with a known station
For example:
Radio Checks
Notes: 3. Replies should be by means of a short and concise report of actual reception using any combination of strength and readability.
4. For example: Loud and clear, very weak but readable or fading and intermittent.
Radio checks can be with a known station. For example:
    MRG91 This is MRG84 Radio check over.
    MRG84 This is MRG91 Good Readable radio check over.
    MRG91 This is MRG84 Loud clear out

## Slide 5
    Alpha Charlie - this is MRG84 radio check - over
    MRG84 - this is MRG77 good readable radio check - over
    MRG77 - this is MRG84 weak readable - out
Radio checks can also be obtained generally
For example:
Radio Checks
Notes: 5. Alternatively radio checks can be obtained by calling generally on the net using the two phonetic code words ALPHA CHARLIE. When a radio check is preceded by Alpha Charlie, it indicates that any station listening may give a reply, for example:
    Alpha Charlie This is MRG84 Radio check over
    MRG84 This is MRG77 Good readable radio check over.
    MRG77 This is MRG84 Weak readable out.

## Slide 6
The call:
  MRG 02 - this is MRV12 - over
  MRV 12 - this is MRG 02 - over
The text:
  MRG 02 - this is MRV 12 - arrange for the mini bus to be sent to this location - over
The ending:
  MRV 12 - this Is MRG 02 - wilco - out
Messages
Notes: Messages
6. Messages sent on the radio consists of 3 distinct elements they are:
  a. The Call. The call is always at the start of a message and is in the following format:
MRG 02 This is MRV 12 over.
MRV 12 This is MRG 02 Ml send over.
  b. The Text. The text is the part of a message which conveys the meaning or the instructions. It may take more than one transmission to pass on the entire message. This is an example of text:
MRG 02 M1 This is MRV 12 Arrange for the mini bus to be sent to this location - over.
  C. The Ending. The ending is used to signify that the message has been understood and action will be taken if necessary, and as the name implies it is the end of that message. For example:
MRV 12 This is MRG 02 Wilco - out
7. In this example, the network control station MRV12 instructed MRG02 to send transport to his location.
MRG 02 replies that the message has been received and understood and that they are complying with the instructions.

## Slide 7
The call:
  G 02 - this is V 12 - over
  V 12 - this is G 02 - over
The text:
  G 02 - this is V 12 - arrange for the mini bus to be sent to this location – over
The ending:
  V 12 - this is G 02 - wilco - out
Abbreviated Callsigns
Fixed Stations
Notes: Abbreviated Callsigns
8. You can see from the above examples that the transmission is dominated by the callsigns. This makes for more difficult and overlong transmissions. To make transmissions shorter, stations may abbreviate their callsigns. This is done by omitting the "MR" part of a callsign. The above example is now shown with the callsigns shortened:
    G 02 This is V 12 over.
    V 12 This is G 02 send over.
    G 02 This is V 12 arrange for minibus to be sent to this location over.
    V 12 This is G 02 Wilco out

## Slide 8
    The call:
    G 02A - this is V 12Z - message - over
    V 12Z - this is G 02A - send your message - over
    The text:
    G 02 A - this is V12 Z - request minibus to pick up party at GRID - TQ 888 999 - over
    The ending:
    V 12Z - this is G 02A - wilco - out
Abbreviated Callsigns
Fixed Stations
Notes: 9. If stations are using callsigns with an extension to the parent callsign, then a message may be as follows:
    G 02A This is V 12Z message over.
    V 12Z This is G 02A send you message over.
    G 02 A This is V12 Z request minibus to pick up party at GRID TQ 888 999 over
    V 12Z This is G 02A wilco out
Note: In this example the proword “Message” was used and indicates that the message may require to be written down by the receiving Station. (The Grid is given as Tango Quebec 888 999)
10. After the initial call between two stations, callsigns may be dropped altogether unless confusion is likely to arise by doing so. However, full callsigns are to be used when first establishing a net.

## Slide 9
Authentication is a way of checking
that a station is genuine
Authentication
Notes: Authentication
11. Authentication, as mentioned earlier, is a method of challenging any station that is using your network.

## Slide 10
Alpha
Bravo
Charlie
Delta
Authentication
Notes: The system used by Air Cadets asks the station to respond to one of four codes:
a. Alpha
b. Bravo
c. Charlie
d. Delta

## Slide 11
Authenticate:
Alpha
MRC 28
Callsign list shows Sqn number as:
378
Station’s Squadron Number
Authentication
Notes: AUTHENTICATE
12. Alpha. The reply to this challenge is the station's Squadron Number.
  Example
  (Reminder, when sending or reading Callsigns they should be pronounced using the Phonetic Alphabet)
  MRC 28 This is MRC 56 Authenticate Alpha Over.
  MRC 56 This is MRC 28 I Authenticate Alpha - 378 Over.
  MRC 28 This is MRC 56 Correct Out.
This means that the station with the callsign MRC 28 is 378 Squadron. The figures used for the authentication should be said as separate numbers. If the Squadron number only consist of one digit that single digit should be given. (Units with a squadron number consisting of only one digit then the reply to either Authentication Alpha or Bravo will be the same). Should a Squadron number include an “F” this should be ignored.
INFORMATION
The proword “Figures” is normally used in front of numbers when sent.
Exceptions to this rule, when figures are always spoken digit by digit
whenever they appear, and without the proword FIGURES are:
(1) Callsigns
(2) Grid references.
(3) Target indications (except that exact multiples of a hundred or a
thousand are pronounced as such).
(4) Authentication
(5) Formal message date time groups (DTGs).

## Slide 12
Callsign list shows Sqn No
as :
Sqn number in reverse
873
Reverse the number
Authentication
Authenticate:
Bravo
MRC 28
Notes: AUTHENTICATE
13. Bravo. The reply to this challenge is the Station’s Squadron number in reverse.
  Example
  MRC 28 This is MRC 56 Authenticate Bravo Over.
  MRC 56 This is MRC 28 I Authenticate Bravo 873 Over.
  MRC 28 This is MRC 56 Correct Out.
This also means that the station with the callsign MRC 28 is 378 Squadron.

## Slide 13
Callsign list shows Sqn No
as :
5
F
The date is 12 April
+
12
=
17
Sqn number added to date
Authentication
Authenticate:
Charlie
MRC 16
Notes: AUTHENTICATE
14. Charlie. The reply to this challenge is state the station's Squadron number added to the date (day of the month). For 5 (F) Squadron on the 12 of April the answer would be 17 (5+12)
  Example
  MRC 16 This is MRC 56 Authenticate Charlie - Over.
  MRC 56 This is MRC 16 I Authenticate Charlie – 17 - Over.
  MRC 16 This is MRC 56 Correct - out
This means that the station with the callsign MRC 16 is 5 (F) Squadron.

## Slide 14
Callsign list shows Sqn No
as :
1374
+
The date is 30 November
30
=
1404
Sqn number added to date
Authentication
Authenticate:
Charlie
MRC 47
Notes: Lets do another one!

## Slide 15
How will it sound?
MRC 16 - this is MRC 56 - authenticate Charlie - over
MRC 56 - this is MRC 16 - I authenticate Charlie 17 - over
MRC 16 - this is MRC 56 - correct - out
Authentication
Notes: This is how an authentication should sound

## Slide 16
The Callsign number is added to the date
92
+
21
=
113
The date is 21 July
Callsign MRV 92
Authentication
Authenticate:
Delta
Notes: AUTHENTICATE
15. Delta. The reply to this challenge is the Call Sign number added to the date (day of the month). For Callsign MRV 92 and on the 21 July the answer would be 113 (92+21)
  Example
  MRV 92 This is MRL 47 Authenticate Delta Over
  MRL 47 This is MRV 92 I Authenticate – 113- Over
  MRV 92 This is MRL 47 Correct Out
Should the reply not be satisfactory, i.e. there is no such squadron shown in the List of Callsigns, all radio traffic and transmissions must be stopped immediately and your Radio Officer I informed.
Authenticating Bravo and Charlie should not normally be used when challenging a mobile unit.
Delta can only be used for Stations who do not have a Squadron number such as Wing and region Callsigns.

## Slide 17
If the reply is wrong the Unit will not be in the Callsign list
Do not contact them again
Refer the matter to your Radio Communications Officer
Authentication
Notes: 16. Should the reply not be satisfactory, i.e. there is no such squadron shown in the List of Call Signs, all radio traffic with that station should be stopped immediately and your Radio Communications Officer informed.

## Slide 18
Mobile Stations only use Alpha and Delta
Special Stations, Wing or Region HQ use only Delta
Authentication
Notes: 17. Authenticating Bravo and Charlie should not normally be used when challenging a mobile unit.

## Slide 19: Any questions?